## Slide 1: Microcontroller & Microprocessor
م . م غيث عبد الودود تقي الكلية التقنية الهندسية / بغداد dr.nasri@mtu.edu.iq
Assistant Lecturer Ghaith A. Taki
Ghaith.taki@gmail.com

## Slide 2
Microcontroller based Design II : The ATmega8 Basic Features (1)

## Slide 3
II: Atmega8 – Basic features
ATmega8 - RISC Architecture
● 130 Instructions – Most Single-clock Cycle Execution
● 32 x 8 General Purpose Working Registers
● 64 x 8 Special Function Registers (I/O Registers)
● Up to 16 MIPS Throughput at 16 MHz
● On-chip 2-cycle Multiplier
Nonvolatile Program and Data Memories
● 8K Bytes of In-System Self-Programmable Flash
10,000 Write/Erase Cycles
● Optional Boot Code Section with Independent Lock Bits
● 512 Bytes EEPROM (100,000 Write/Erase Cycles)
● 1K Byte Internal SRAM
● Programming Lock for Software Security

## Slide 4
Peripheral Features
● Two 8-bit Timer/Counters
● One 16-bit Timer/Counter with Capture Mode
● Real Time Counter with Separate Oscillator
● Three PWM Channels
● 6-channel ADC with 10 resp 8 Bit resolution (TQFP: 8 channels)
● Two-wire Serial Interface (TWI)
● Programmable Serial USART
● Master/Slave SPI Serial Interface
● Programmable Watchdog Timer with On-chip Oscillator
● On-chip Analog Comparator

## Slide 5
II: Atmega8 – Basic features
Special Microcontroller Features
● Programmable Brown-out Detection
● Internal Calibrated RC Oscillator
● External and Internal Interrupt Sources
● Five Sleep Modes
I/O and Packages
● 23 Programmable I/O Lines
● 28-lead PDIP, 32-lead TQFP, and 32-pad MLF

## Slide 6
II: Atmega8 – Basic features
Operating Voltages
● 2.7 - 5.5V (ATmega8L)
● 4.5 - 5.5V (ATmega8)
Speed Grades
● 0 - 8 MHz (ATmega8L)
● 0 - 16 MHz (ATmega8)
Power Consumption at 4 Mhz, 3V, 25°C
● Active: 3.6 mA
● Idle Mode: 1.0 mA
● Power-down Mode: 0.5 μA

## Slide 7
II: Atmega8 – Basic features
ATmega8 Pinout and Packages (DIP and TQFP)

## Slide 8
II: Atmega8 – Basic features
ATmega8 Core Architecture
● Seperate Instruction and Data Memories (Harvard)
● all 32 General Purpose Registers connected to ALU
● I/O Modules connected to Data Bus and accessible via Special Function Registers
Mega8 CPU Core

## Slide 9
II: Atmega8 – Basic features

## Slide 10
II: Atmega8 – Basic features
Harvard architecture
● Separate storage and signal pathways for instructions and data.
● History: Harvard Mark I
relay-based computer
● word width, timing, and implementation technology of instruction and data memories can differ.
● Contrast: ‘Von Neumann’ - architecture: Instructions and data use the same signal pathways and memory.

## Slide 11
II: Atmega8 – Basic features
Harvard architecture
● Ability to fetch the next instruction at the same time it completes the current instruction.
● Speed is gained at the expense of more complex electrical circuitry.
In a computer with Harvard architecture, the CPU can read
an instruction and data from memory at the same time.

## Slide 12
II: Atmega8 – Basic features
Pin and Port Overview:
GND: Ground (0V)
VCC: Digital Supply Voltage (2,7 – 5,5V)
AVCC: Analog Supply Voltage
connect to low-pass filtered VCC
AREF: Analog Reference Voltage, usually AVCC
/Reset: Low level on this pin will generate a reset
Port B, Port C, Port D:
General Purpose 8 Bit bidirectional I/O - Ports,
optional internal pullup-resistors when configured as input
output source capability: 20mA
Special Functions of the Ports available as configured using the SFRs:
Port D: Uart, external Interrupts, Analog Comparator
Port B: External Oscillator/Crystal, SPI
Port C: A/D converters, TWI

## Slide 13
II: Atmega8 – Basic features
Memory organization

## Slide 14
II: Atmega8 – Basic features
AVR Memory organization:
● Program Flash Memory:
On-chip, in system programmable
8 Kbytes, organized in 4K 16 bit words
Program Counter (PC) = 12 bits
Accessible via special instructions: LPM, SPM
Boot Loader support: Boot Flash Section,
SPM can be executed only from Boot Flash

## Slide 15
II: Atmega8 – Basic features
AVR Memory organization:
● EEPROM - Memory:
  512 Bytes, single Bytes can be read and written
  Special EEPROM read and write procedure using SFRs:
  EEPROM Address Register, EEPROM Data Register,
  EEPROM Control Register
  C – Library Functions available
  Precautions to prevent EEPROM memory corruption:
  ● no flash memory or interrupt operations
  ● stable power supply

## Slide 16
II: Atmega8 – Basic features
AVR Memory organization:
● SRAM Data Memory:
32 GPR’s and
64 SFR’s mapped
to SRAM memory space
SFR’s accessed
via in / out instructions
(I/O-registers)
1 Kbytes of internal
SRAM can be accessed
from address 0x060
to address 0x45f
5 Direct and indirect addressing modes

## Slide 17
II: Atmega8 – Basic features
AVR Memory organization:
● General Purpose Registers:
Although not being physically
implemented as SRAM locations,
GPR’s can be accessed
by SRAM locations
X, Y and Z 16-bit registers
can be used for indirect addressing
ALU - Input / output schemes:
one 8-bit operand, 8-bit result
two 8-bit operands, 8-bit result
two 8-bit operands, 16-bit result
one 16-bit operand, 16-bit result

## Slide 18
II: Atmega8 – Basic features
I/O Memory (SFR) Overview

## Slide 19
II: Atmega8 – Basic features
I/O Memory (SFR) Overview

## Slide 20
II: Atmega8 – Basic features
Important I/O Registers:
SREG – Status Register
Bit 7 – I: Global Interrupt Enable
Bit 6 – T: Bit Copy Storage
Bit 5 – H: Half Carry Flag
Bit 4 – S: Sign Bit
Bit 3 – V: Two’s Complement Overflow Flag
Bit 2 – N: Negative Flag
Bit 1 – Z: Zero Flag
Bit 0 – C: Carry Flag

## Slide 21
II: Atmega8 – Basic features
Important I/O Registers:
Stack Pointer (SPH and SPL)
● Stack is a LIFO buffer located in SRAM
● Stack Pointer addresses the current location
● Push and pop instructions write / read from Stack
● Enter or return from subroutines / interrupt routines:
Address and Parameters transferred via Stack

## Slide 22
II: Atmega8 – Basic features
Clock Options

## Slide 23
II: Atmega8 – Basic features
System Clock Options:

## Slide 24
II: Atmega8 – Basic features
System Clock Options:
● Clock Muliplexer selects the clock
source according to FUSE settings
● Clock Control Unit distributes clocks
clocks can be halted to reduce power
consumption
● CPU Clock: CPU, ALU, GPRs
● I/O Clock: Ports, Timers, SPI, UART
● ADC Clock: seperate cock for ADC
noise reduction in sleep mode
● Asynchronous Timer Clock:
external 32kHz Crystal for realtime clock,
keeps timer module running during sleep mode

## Slide 25
II: Atmega8 – Basic features
System Clock Options - FUSE bits:
● The four CKSEL Bits of the FUSE – Byte select the main Clock Source
● The startup time to stabilize power supply and oscillator can be changed with the SUT fuses
● The device is shipped with CKSEL = 0001 ( 1 MHZ internal RC oscillator )
and SUT = 10 ( slowly rising power, 65ms )

## Slide 26
II: Atmega8 – Basic features
System Clock Options - using an external crystal:
● CKOPT influences the output swing of the inverting oscillator amplifier
(1 = full rail to rail swing, 0 = power save mode)
● For crystals from 3 – 8 MHz set CKOPT = 1 and CKSEL3..1 = 111

## Slide 27
II: Atmega8 – Basic features
System Clock Options - using the internal RC oscillator
  ● Fixed 1, 2, 4 or 8 MHz clock
  ● works without external components
  ● changes with temperature and operating voltage
detailed information on other clock options, startup times, calibration
is found in the ATmega8 data sheet, pp. 23

## Slide 28
II: Atmega8 – Basic features
I/O Ports

## Slide 29
II: Atmega8 – Basic features
I/O Ports
● General Purpose IO : Data Direction Input or Output
● Internal Pullup can be used for Input Pins
● Output driver can source 20mA current
● protection diodes to GND and VCC

## Slide 30
II: Atmega8 – Basic features
I/O Ports
● 3 I/O-Registers for each port:
Data Register (r/w):
PORTB, PORTC, PORTD
Data Direction Register (r/w):
DDRB, DDRC, DDRD
Port Input Pin Register (r):
PINB, PINC, PIND
The Bits of these registers set the configuration for one Port Pin.

## Slide 31
II: Atmega8 – Basic features
I/O Ports
General Digital IO
Logic of GPIO-Ports:
DDx
PORTx
PINx
Common to all Ports:
Pullup disable (PUD),
SLEEP

## Slide 32
II: Atmega8 – Basic features
I/O Ports – Configuration and usage
C-Example 1 - Configure Pin B3 as output, set output level to VCC:
DDRB |= (1<<3); PORTB |= (1<<3);
C-Example 2 - Configure Pin D2 as input with pullup, read pin value:
DDRD &= ~(1<<2); PORTD |= (1<<2); uint8_t x = PIND & (1<<2);

## Slide 33
II: Atmega8 – Basic features
Alternate Port functions Port B

## Slide 34
II: Atmega8 – Basic features
Alternate Port functions Port C

## Slide 35
II: Atmega8 – Basic features
Alternate Port functions Port D

## Slide 36
II: Atmega8 – Basic features
Reset- and Interrupt Handling

## Slide 37
II: Atmega8 – Basic features
Interrupt Processing
● several Interrupt Sources:
External Interrupts, Timer, Bus-Peripherals,
ADC, EEPROM
● individual Interrupt-Enable bits in the SFR‘s
● global interrupt enable Bit in SREG,
set with sei() and clear with cli() instruction
● flagged (remembered) and non-flagged interrupt sources
● lowest addresses in program memory reserved
for the interrupt vector table
● higher priority interrupts have lower addresses

## Slide 38
II: Atmega8 – Basic features
Reset-Vector and
Interrupt-Vectors
● Word addresses
0, 1 – 19 in Flash Ram
● When a reset or
interrupt occurs,
the CPU calls
the address
● Install an Interrupt
Handler: modify
the vector table to
jump to your user-
handler
● return from interrupt:
reti

## Slide 39
II: Atmega8 – Basic features
Reset-Vector and
Interrupt-Vectors
● example shows
full featured
vector table
● 19 handlers installed
● program execution
after reset:
jmp RESET ($013)
● Main program is
located at $013,
beyond the vectors

## Slide 40
II: Atmega8 – Basic features
Reset- and Interrupt- Vectors
● Reset vector can be set to the Bootloader section using the
BOOTRST fuse bit
● Interrupt vectors can be set to the Bootloader section using the IVSEL bit of the General Interrupt Contol Register

## Slide 41
II: Atmega8 – Basic features
AVR Reset Sources:

## Slide 42
II: Atmega8 – Basic features
Reset Sources:
• Power-on Reset: supply voltage is below the Power-on Reset threshold
• External Reset: low level is present on /RESET – input pin
• Watchdog Reset: Watchdog Timer enabled and period expires
• Brown-out Reset: Brown-out Detector enabled and supply voltage below threshold
MCUCSR provides information on which reset source caused a CPU reset

## Slide 43
II: Atmega8 – Basic features
Reset Voltage Thresholds

## Slide 44
II: Atmega8 – Basic features
Reset Voltage Thresholds:
Example:
Power-on Reset
Example:
Brown Out Reset

## Slide 45
II: Atmega8 – Basic features
External Interrupts Int0 and Int1:
• Int0 connected to PD2
• Int1 connected to PD3
• asynchronous operation: can wake up CPU
• rising/falling edge or low level can trigger interrupt,
defined by Interrupt Sense control – bits of MCUCR SFU

## Slide 46
II: Atmega8 – Basic features
External Interrupts Int0 and Int1:
• Int0 and Int1 have to be enabled by the GICR (+ I-bit in SREG)
• flagged interrupts: General Interrupt Flag Register (GIFR)
indicates when an interrupt request happened
• flags are cleared by executing the interrupt service routine (ISR)
or by writing 1 to the flag bit of GIFR

## Slide 47
II: Atmega8 – Basic features
8-bit Timer / Counter0
• 10-bit clock Prescaler
timer-clk (t0) = clk (IO) / prescaler
• External clock source T0 connected to PD4
cannot be prescaled, clk(ext) <= clk (IO) / 2.5

## Slide 48
II: Atmega8 – Basic features
8-bit Timer / Counter0 - prescaler operation
No prescaler
MAX=0xff
BOTTOM=0
Prescaler = 8

## Slide 49
II: Atmega8 – Basic features
8-bit Timer / Counter0 usage
Timer/Counter0 Control Register (TCCR0), Bits CS02-CS00
select Clock Source and Prescaler Value :

## Slide 50
II: Atmega8 – Basic features
8-bit Timer / Counter0 usage
Timer/Counter0 Register (TCNT0) :
read/write, incremented per CLK cycle, overflow: 0xff
• A Reload-Value is used to fine-tune the interrupt interval
• write Reload-Value to TCNT0 in the ISR

## Slide 51
II: Atmega8 – Basic features
8-bit Timer / Counter0 usage
Timer Interrupt Flag Register (TIFR) :
TOV0 indicates a Timer0 overflow, cleared by hardware when
the ISR is executed or by writing 1 to the flag
Timer/Counter Interrupt Mask Register (TIMSK) :
Bit 0 : Timer 0 interrupt enable
set 1 to enable timer 0 overflow interrupt ( + I-Bit in SREG)

## Slide 52
8086
MICROPROCESSOR

## Slide 53: 8086 Microprocessor

## Slide 55: 8086 Features
• 16-bit Arithmetic Logic Unit
• 16-bit data bus (8088 has 8-bit data bus)
• 20-bit address bus - 220 = 1,048,576 = 1 meg
The address refers to a byte in memory. In the 8088, these bytes come in on
the 8-bit data bus. In the 8086, bytes at even addresses come in on the low
half of the data bus (bits 0-7) and bytes at odd addresses come in on the upper
half of the data bus (bits 8-15).
The 8086 can read a 16-bit word at an even address in one operation and at an
odd address in two operations. The 8088 needs two operations in either case.
The least significant byte of a word on an 8086 family microprocessor is at the
lower address.

## Slide 56
Simplified CPU Design

## Slide 57
Intel 16-bit Registers

## Slide 58: 8086 Architecture
  • The 8086 has two parts, the Bus Interface Unit (BIU) and the
  Execution Unit (EU).
  • The BIU fetches instructions, reads and writes data, and computes the
  20-bit address.
  • The EU decodes and executes the instructions using the 16-bit ALU.
  • The BIU contains the following registers:
    IP - the Instruction Pointer
    CS - the Code Segment Register
    DS - the Data Segment Register
    SS - the Stack Segment Register
    ES - the Extra Segment Register
The BIU fetches instructions using the CS and IP, written CS:IP, to contract
the 20-bit address. Data is fetched using a segment register (usually the DS)
and an effective address (EA) computed by the EU depending on the
addressing mode.

## Slide 59
The EU contains the following 16-bit registers:
        AX - the Accumulator
        BX - the Base Register
        CX - the Count Register
        DX - the Data Register
        SP - the Stack Pointer \ defaults to stack segment
        BP - the Base Pointer /
        SI - the Source Index Register
        DI - the Destination Register
These are referred to as general-purpose registers, although, as seen by
their names, they often have a special-purpose use for some instructions.
The AX, BX, CX, and DX registers can be considers as two 8-bit registers, a
High byte and a Low byte. This allows byte operations and compatibility with
the previous generation of 8-bit processors, the 8080 and 8085. 8085 source
code could be translated in 8086 code and assembled. The 8-bit registers are:
        AX --> AH,AL
        BX --> BH,BL
        CX --> CH,CL
        DX --> DH,DL

## Slide 61: Registers

## Slide 62: 8086 Programmer’s Model
ES
CS
SS
DS
IP
AH
BH
CH
DH
AL
BL
CL
DL
SP
BP
SI
DI
FLAGS
AX
BX
CX
DX
Extra Segment
Code Segment
Stack Segment
Data Segment
Instruction Pointer
Accumulator
Base Register
Count Register
Data Register
Stack Pointer
Base Pointer
Source Index Register
Destination Index Register
BIU registers
(20 bit adder)
EU registers

## Slide 63
8086/88 internal registers 16 bits (2 bytes each)
AX, BX, CX and DX are two
bytes wide and each byte can
be accessed separately
These registers are used as
memory pointers.
Flags will be discussed later
Segment registers are used
as base address for a segment
in the 1 M byte of memory

## Slide 64
The 8086/8088 Microprocessors: Registers
Registers
  Registers are in the CPU and are referred to by specific names
  Data registers
    Hold data for an operation to be performed
    There are 4 data registers (AX, BX, CX, DX)
  Address registers
    Hold the address of an instruction or data element
    Segment registers (CS, DS, ES, SS)
    Pointer registers (SP, BP, IP)
    Index registers (SI, DI)
  Status register
    Keeps the current status of the processor
    On an IBM PC the status register is called the FLAGS register
  In total there are fourteen 16-bit registers in an 8086/8088

## Slide 65
Data Registers: AX, BX, CX, DX
Instructions execute faster if the data is in a register
AX, BX, CX, DX are the data registers
Low and High bytes of the data registers can be accessed separately
  AH, BH, CH, DH are the high bytes
  AL, BL, CL, and DL are the low bytes
Data Registers are general purpose registers but they also perform special functions
AX
  Accumulator Register
  Preferred register to use in arithmetic, logic and data transfer instructions because it generates the shortest Machine Language Code
  Must be used in multiplication and division operations
  Must also be used in I/O operations

## Slide 66
BX
  Base Register
  Also serves as an address register
CX
  Count register
  Used as a loop counter
  Used in shift and rotate operations
DX
  Data register
  Used in multiplication and division
  Also used in I/O operations

## Slide 67
Pointer and Index Registers
Contain the offset addresses of memory locations
Can also be used in arithmetic and other operations
SP: Stack pointer
  Used with SS to access the stack segment
BP: Base Pointer
  Primarily used to access data on the stack
  Can be used to access data in other segments
SI: Source Index register
  is required for some string operations
  When string operations are performed, the SI register points to memory locations in the data segment which is addressed by the DS register. Thus, SI is associated with the DS in string operations.

## Slide 68
DI: Destination Index register
  is also required for some string operations.
  When string operations are performed, the DI register points to memory locations in the data segment which is addressed by the ES register. Thus, DI is associated with the ES in string operations.
The SI and the DI registers may also be used to access data stored in arrays

## Slide 69
Segment Registers - CS, DS, SS and ES
Are Address registers
Store the memory addresses of instructions and data
Memory Organization
  Each byte in memory has a 20 bit address starting with 0 to 220-1 or 1 meg of addressable memory
  Addresses are expressed as 5 hex digits from 00000 - FFFFF
  Problem: But 20 bit addresses are TOO BIG to fit in 16 bit registers!
  Solution: Memory Segment
    Block of 64K (65,536) consecutive memory bytes
    A segment number is a 16 bit number
    Segment numbers range from 0000 to FFFF
    Within a segment, a particular memory location is specified with an offset
    An offset also ranges from 0000 to FFFF

## Slide 71: Segmented Memory
Segmented memory addressing: absolute (linear) address is a combination of a 16-bit segment value added to a 16-bit offset
linear addresses
one segment

## Slide 72
Memory Address Generation
The BIU has a dedicated adder for determining physical memory addresses
Intel
Physical Address (20 Bits)
Adder
Segment Register (16 bits)
0 0 0 0
Offset Value (16 bits)

## Slide 73
Example Address Calculation
If the data segment starts at location 1000h and a data reference contains the address 29h where is the actual data?
Intel
Offset:
0 0 0 0 0 0 0 0 0 0 1 0 1 0 0 1
2
9
0 0 0 1 0 0 0 0 0 0 0 0 0 0 0 0
0 0 0 0
Segment:
0 0 0 1 0 0 0 0 0 0 0 0 0 0 1 0
1 0 0 1
Address:

## Slide 74
Segment:Offset Address
Logical Address is specified as segment:offset
Physical address is obtained by shifting the segment address 4 bits to the left and adding the offset address
Thus the physical address of the logical address A4FB:4872 is
      A4FB0
      + 4872
      A9822

## Slide 76: Your turn . . .
What linear address corresponds to the segment/offset address 028F:0030?
028F0 + 0030 = 02920
Always use hexadecimal notation for addresses.

## Slide 77: Your turn . . .
What segment addresses correspond to the linear address 28F30h?
Many different segment-offset addresses can produce the linear address 28F30h. For example:
28F0:0030, 28F3:0000, 28B0:0430, . . .

## Slide 78
The Code Segment
Memory
Segment Register
Offset
Physical or
Absolute Address
0
+
CS:
IP
0400H
0056H
4000H
4056H
0400
0056
04056H
The offset is the distance in bytes from the start of the segment.
The offset is given by the IP for the Code Segment.
Instructions are always fetched with using the CS register.
CS:IP = 400:56
Logical Address
0H
0FFFFFH
The physical address is also called the absolute address.

## Slide 79
The Data Segment
Memory
Segment Register
Offset
Physical Address
+
DS:
SI
05C0
0050
05C00H
05C50H
05C0
0
0050
05C50H
Data is usually fetched with respect to the DS register.
The effective address (EA) is the offset.
The EA depends on the addressing mode.
DS:EA
0H
0FFFFFH

## Slide 80
The Stack Segment
Memory
Segment Register
Offset
Physical Address
+
SS:
SP
0A00
0100
0A000H
0A100H
0A00
0
0100
0A100H
The stack is always referenced with respect to the stack segment register.
The stack grows toward decreasing memory locations.
The SP points to the last or top item on the stack.
PUSH - pre-decrement the SP
POP - post-increment the SP
The offset is given by the SP register.
SS:SP
0H
0FFFFFH

## Slide 81
Flags
Carry flag
Parity flag
Auxiliary flag
Zero
Overflow
Direction
Interrupt enable
Trap
Sign
6 are status flags
3 are control flag

## Slide 82: Flag Register
CF (carry) Contains carry from leftmost bit following arithmetic, also contains last bit from a shift or rotate operation.
Flag |  |  |  |  | O | D | I | T | S | Z |  | A |  | P |  | C
Bit no. | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Conditional flags:
  They are set according to some results of arithmetic operation. You do not need to alter the value yourself.
Control flags:
  Used to control some operations of the MPU. These flags are to be set by you in order to achieve some specific purposes.

## Slide 83: Flag Register
OF (overflow) Indicates overflow of the leftmost bit during arithmetic.
DF (direction) Indicates left or right for moving or comparing string data.
IF (interrupt) Indicates whether external interrupts are being processed or ignored.
TF (trap) Permits operation of the processor in single step mode.

## Slide 84
SF (sign) Contains the resulting sign of an arithmetic operation (1=negative)
ZF (zero) Indicates when the result of arithmetic or a comparison is zero. (1=yes)
AF (auxiliary carry) Contains carry out of bit 3 into bit 4 for specialized arithmetic.
PF (parity) Indicates the number of 1 bits that result from an operation.

## Slide 87
Addressing modes
  Register and immediate modes we have already seen
  MOV AX,1
  MOV BX,AX
  register immediate

## Slide 88: 3F03 - 80x86 assembler
Typical addressing modes
  Absolute address mode
  MOV AX,[0200]
  value stored in memory location DS:0200

## Slide 89: 3F03 - 80x86 assembler
Typical addressing modes
  Register indirect
  MOV AX,[BX]
  value stored at address contained in DS:BX

## Slide 90: 3F03 - 80x86 assembler
Typical addressing modes
  Displacement
  MOV DI,4
  MOV AX,[0200+DI]
  value stored at DS:0204

## Slide 91: 3F03 - 80x86 assembler
Typical addressing modes
  Indexed
MOV BX,0200
  MOV DI,4
  MOV AX,[BX+DI]
  value stored at DS:0204

## Slide 92: 3F03 - 80x86 assembler
Typical addressing modes
  Memory indirect
MOV DI,0204
MOV BX,[DI]
  MOV AX,[BX]
  If DS:0204 contains 0256,
  then AX will contain
  whatever is stored at
  DS:0256

## Slide 93: 3F03 - 80x86 assembler
Typical addressing modes
  Memory indirect
MOV DI,0204
MOV BX,[DI]
  MOV AX,[BX]
  If DS:0204 contains 0256,
  then AX will contain
  whatever is stored at
  DS:0256

## Slide 94: 8086 in Maximum Mode
The IBM PC is a maximum mode 8088 system. When an 8086/8088 is used
in the maximum mode (MN/MX pin grounded) it requires the use of an 8288
Bus Controller. The system can support multiple processors on the system
bus by the use of an 8289 Bus Arbiter.
The following signals now come from the 8288: ALE, DT/R’, DEN, and INTA’.
The M/IO’, RD’, and WR’ signals are replaced by:
  MRDC’ - memory read command
  MWTC’ - memory write command
  IORC’ - I/O read command
  IOWC’ - I/O write command
  AMWC’ - Advanced memory write command
  AIOWC’ - Advanced I/O write command
The advanced commands become active earlier in the cycle to give devices
an earlier indication of a write operation.
IV-1

## Slide 95: 8086 Maximum Mode
When in the maximum mode, the 8086/8088 has 3 status lines that are
connected to the 8288 and provide it with the information it needs to
generate the system bus signals. The information provided by the status
bits is as follows.
S2’ S1’ S0’ operation signal
0 0 0 Interrupt Acknowledge INTA’
0 0 1 Read I/O port IORC’
0 1 0 Write I/O port IOWC’, AIOWC’
0 1 1 Halt none
1 0 0 Instruction Fetch MRDC’
1 0 1 Read Memory MRDC’
1 1 0 Write Memory MWTC’, AMWC’
1 1 1 Passive none
IV-2

## Slide 96: Direct Memory Access - DMA
DMA allows data to go between memory and a peripheral, such as a disk
drive, without going through the cpu.
The DMA controller takes over the address bus, data bus, and control bus.
The 8237A DMA Controller is a commonly used device and is in the IBM PC.
Figure 11-4 is a simplified block diagram showing the use of a DMA controller.
For example, to read a disk file the following operations occur.
  1. Send a series of commands to the disk controller to find and read a
  block of data.
  2. When the controller has the first byte of the block, it sends a DMA
  request DREQ to the DMA controller.
  3. If that input of the DMA controller is unmasked, the DMA controller
  sends a hold-request HQR to the cpu.
  4. The cpu responds with a hold-acknowledge HLDA and floats its buses.
  5. The DMA controller then takes control of the buses.
  6. The DMA controller sends out the memory address and DMA
  acknowledge DACK0 to the disk controller.
  7. The DMA controller asserts the MEMW’ and IOR’ lines.
IV-4

## Slide 97: Memory
IV-6
Terminology
Volatile - data is lost when power is turned off.
Nonvolatile - retains data when powered off.
Random Access - all data locations accessed in the same amount of time.
Sequential Access - data accessed in varying amounts of time, e.g., tape.
ROM - Read Only Memory.
RAM - Random Access Memory
By convention, RAM in a PC is really Read/Write Memory and ROM
(EPROM) in a PC, although random access memory, is not referred to
as RAM.
Examples
  VOLATILE NONVOLATILE
Static RAM ROM, PROM, EPROM, EEPROM, FLASH
Dynamic RAM Disk, tape
        Magnetic core, magnetic bubble

## Slide 98: Interface 8086 to 6116 static RAM
8086
A
____
BHE
ALE
A(10-0)
D(7-0)
__
R/W
OE*
CS*
A(10-0)
__
R/W
OE*
CS*
D
D(7-0)
20
Latch
Addr
Decoder
A(11-1)
21
A0, BHE*
A(19-12)
A(11-1)
__
M/IO
___
RD
___
WR
READY
low byte
(even)
hi byte
(odd)
D(7-0)
D(15-8)
16
A0
RAMCS*
MEM*
BHE*
Wait
State Gen
6116 (2K x8)

## Slide 99: Introduction to 8086 Assembly Language Programming

## Slide 100: What Is Assembly Language
Machine-Specific Programming Language
  one-one correspondence between statements and native machine language
  matches machine instruction set and architecture
IBM-PC Assembly Language
  refers to 8086, 8088, 80186, 80286, 80386, 80486, and Pentium Processors

## Slide 101: What Is An Assembler?
Systems Level Program
  translates assembly language source code to machine language
    object file - contains machine instructions, initial data, and information used when loading the program
    listing file - contains a record of the translation process, line numbers, addresses, generated code and data, and a symbol table

## Slide 102: Why Learn Assembly Language?
Learn how a processor works
Understand basic computer architecture
Explore the internal representation of data and instructions
Gain insight into hardware concepts
Allows creation of small and efficient programs
Allows programmers to bypass high-level language restrictions
Might be necessary to accomplish certain operations

## Slide 103: Data Representation
Binary 0-1
  represents the state of electronic components used in computer systems
Bit - Binary digit
Byte - 8 Bits
  smallest addressable memory location (on the IBM-PC)
Word - 16 Bits
  Each architecture may define its own “wordsize”
Doubleword - 32 Bits
Quadword - 64 Bits
Nybble - 4 Bits

## Slide 104: Numbering Systems
Binary - Base 2
  0, 1
Octal - Base 8
  0, 1, 2, … 7
Decimal - Base 10
  0, 1, 2, …, 9
Hexadecimal (Hex)
  0, 1, …, 9, A, B, …, F
Raw Binary format
  All information is coded for internal storage
  Externally, we may choose to express the information in any numeration system, or in a decoded form using other symbols

## Slide 105: Decoding a Byte
Raw
  01010000b
Hex
  50h
Octal
  1208
Decimal
  80d
Machine Instruction
  Push AX
ASCII Character code
  ‘P’
Integer
  80 (eighty)
BCD
  50 (fifty)
Custom code ???

## Slide 106: Machine Language
A language of numbers, called the Processor’s Instruction Set
  The set of basic operations a processor can perform
Each instruction is coded as a number
Instructions may be one or more bytes
Every number corresponds to an instruction

## Slide 107: Assembly Language vs Machine Language Programming
Machine Language Programming
  Writing a list of numbers representing the bytes of machine instructions to be executed and data constants to be used by the program
Assembly Language Programming
  Using symbolic instructions to represent the raw data that will form the machine language program and initial data constants

## Slide 108: Assembly Language Instructions
Mnemonics represent Machine Instructions
  Each mnemonic used represents a single machine instruction
  The assembler performs the translation
Some mnemonics require operands
  Operands provide additional information
    register, constant, address, or variable
Assembler Directives

## Slide 109: 8086 Instruction - Basic Structure
Label Operator Operand[s] ;Comment
Label - optional alphanumeric string
1st character must be a-z,A-Z,?,@,_,$
Last character must be :
Operator - assembly language instruction
mnemonic: an instruction format for humans
Assembler translates mnemonic into hexadecimal opcode
example: mov is f8h
Operand[s] - 0 to 3 pieces of data required by instruction
Can be several different forms
Delineated by commas
immediate, register name, memory data, memory address
Comment - Extremely useful in assembler language
These fields are separated by White Space (tab, blank, \n, etc.)

## Slide 110: 8086 Instruction - Example
Label Operator Operand[s] ;Comment
INIT: mov ax, bx ; Copy contents of bx into ax
Label - INIT:
Operator - mov
Operands - ax and bx
Comment - alphanumeric string between ; and \n
Not case sensitive
Unlike other assemblers, destination operand is first
mov is the mnemonic that the assembler translates into an opcode

## Slide 111: Assembler Language Segment Types
Stack
  For dynamic data storage
  Source file defines size
  Must have exactly 1
Data
  For static data Storage
  Source file defines size
  Source file defines content (optional)
  Can have 0 or more
Code
  For machine Instructions
  Must have 1 or more

## Slide 112: Using MASM Assembler
to get help:
  C:\> masm /h
Can just invoke MASM with no arguments:
  C:\> masm
  Source Filename [.ASM]: hello
  Object Filename [HELLO.OBJ]:
  Source Listing [NUL.LST]:
  Cross Reference [NUL.CRF]:
.ASM - Assembler source file prepared by programmer
.OBJ - Translated source file by assembler
.LST - Listing file, documents “Translation” process
        Errors, Addresses, Symbols, etc
.CRF – Cross reference file

## Slide 113: x86 Instruction Set Summary (Data Transfer)
CBW ;Convert Byte to Word AL  AX
CWD ;Convert Word to Double in AX DX,AX
IN ;Input
LAHF ;Load AH from Flags
LDS ;Load pointer to DS
LEA ;Load EA to register
LES ;Load pointer to ES
LODS ;Load memory at SI into AX
MOV ;Move
MOVS ;Move memory at SI to DI
OUT ;Output
POP ;Pop
POPF ;Pop Flags
PUSH ;Push
PUSHF ;Push Flags
SAHF ;Store AH into Flags
STOS ;Store AX into memory at DI
XCHG ;Exchange
XLAT ;Translate byte to AL

## Slide 114: x86 Instruction Set Summary (Arithmetic/Logical)
AAA ;ASCII Adjust for Add in AX
AAD ;ASCII Adjust for Divide in AX
AAM ;ASCII Adjust for Multiply in AX
AAS ;ASCII Adjust for Subtract in AX
ADC ;Add with Carry
ADD ;Add
AND ;Logical AND
CMC ;Complement Carry
CMP ;Compare
CMPS ;Compare memory at SI and DI
DAA ;Decimal Adjust for Add in AX
DAS ;Decimal Adjust for Subtract in AX
DEC ;Decrement
DIV ;Divide (unsigned) in AX(,DX)
IDIV ;Divide (signed) in AX(,DX)
MUL ;Multiply (unsigned) in AX(,DX)
IMUL ;Multiply (signed) in AX(,DX)
INC ;Increment

## Slide 115: x86 Instruction Set Summary (Arithmetic/Logical Cont.)
NEG ;Negate
NOT ;Logical NOT
OR ;Logical inclusive OR
RCL ;Rotate through Carry Left
RCR ;Rotate through Carry Right
ROL ;Rotate Left
ROR ;Rotate Right
SAR ;Shift Arithmetic Right
SBB ;Subtract with Borrow
SCAS ;Scan memory at DI compared to AX
SHL/SAL ;Shift logical/Arithmetic Left
SHR ;Shift logical Right
SUB ;Subtract
TEST ;AND function to flags
XLAT ;Translate byte to AL
XOR ;Logical Exclusive OR

## Slide 116: x86 Instruction Set Summary (Control/Branch Cont.)
CALL ;Call
CLC ;Clear Carry
CLD ;Clear Direction
CLI ;Clear Interrupt
ESC ;Escape (to external device)
HLT ;Halt
INT ;Interrupt
INTO ;Interrupt on Overflow
IRET ;Interrupt Return
JB/JNAE ;Jump on Below/Not Above or Equal
JBE/JNA ;Jump on Below or Equal/Not Above
JCXZ ;Jump on CX Zero
JE/JZ ;Jump on Equal/Zero
JL/JNGE ;Jump on Less/Not Greater or Equal
JLE/JNG ;Jump on Less or Equal/Not Greater
JMP ;Unconditional Jump
JNB/JAE ;Jump on Not Below/Above or Equal
JNBE/JA ;Jump on Not Below or Equal/Above
JNE/JNZ ;Jump on Not Equal/Not Zero
JNL/JGE ;Jump on Not Less/Greater or Equal

## Slide 117: x86 Instruction Set Summary (Control/Branch)
JNLE/JG ;Jump on Not Less or Equal/Greater
JNO ;Jump on Not Overflow
JNP/JPO ;Jump on Not Parity/Parity Odd
JNS ;Jump on Not Sign
JO ;Jump on Overflow
JP/JPE ;Jump on Parity/Parity Even
JS ;Jump on Sign
LOCK ;Bus Lock prefix
LOOP ;Loop CX times
LOOPNZ/LOOPNE ;Loop while Not Zero/Not Equal
LOOPZ/LOOPE ;Loop while Zero/Equal
NOP ;No Operation (= XCHG AX,AX)
REP/REPNE/REPNZ ;Repeat/Repeat Not Equal/Not Zero
REPE/REPZ ;Repeat Equal/Zero
RET ;Return from call
SEG ;Segment register
STC ;Set Carry
STD ;Set Direction
STI ;Set Interrupt
TEST ;AND function to flags
WAIT ;Wait

## Slide 118: Assembler Directives
end label end of program, label is entry point
proc far|near begin a procedure; far, near keywords specify if procedure in different code segment (far), or same code segment (near)
endp end of procedure
page set a page format for the listing file
title title of the listing file
.code mark start of code segment
.data mark start of data segment
.stack set size of stack segment

## Slide 119: Assembler Directives
db define byte
dw define word (2 bytes)
dd define double word (4 bytes)
dq define quadword (8 bytes)
dt define tenbytes
equ equate, assign numeric expression to a name
Examples:
db 100 dup (?) define 100 bytes, with no initial values for bytes
db “Hello” define 5 bytes, ASCII equivalent of “Hello”.
maxint equ 32767
count equ 10 * 20 ; calculate a value (200)

## Slide 120: Program Example
;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;
; ;
; This is an example program. It prints the ;
; character string "Hello World" to the DOS standard output ;
; using the DOS service interrupt, function 9. ;
; ;
;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;
hellostk SEGMENT BYTE STACK 'STACK' ;Define the stack segment
DB 100h DUP(?) ;Set maximum stack size to 256 bytes (100h)
hellostk ENDS
hellodat SEGMENT BYTE 'DATA' ;Define the data segment
dos_print EQU 9 ;define a constant via EQU
strng DB 'Hello World',13,10,'$' ;Define the character string
hellodat ENDS
hellocod SEGMENT BYTE 'CODE' ;Define the Code segment
START: mov ax, SEG hellodat ;ax <-- data segment start address
mov ds, ax ;ds <-- initialize data segment register
mov ah, dos_print ;ah <-- 9 DOS 21h string function
mov dx,OFFSET strng ;dx <-- beginning of string
int 21h ;DOS service interrupt
mov ax, 4c00h ;ax <-- 4c DOS 21h program halt function
int 21h ;DOS service interrupt
hellocod ENDS
END START ; ‘END label’ defines program entry

## Slide 121: Another Way to define Segments
;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;
; Use 'assume' directive to define segment types ;
; ;
;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;
hellostk SEGMENT ;Define a segment
DB 100h DUP(?)
hellostk ENDS
hellodat SEGMENT ;define a segment
dos_print EQU 9 ;define a constant
strng DB 'Hello World',13,10,'$' ;Define the character string
hellodat ENDS
hellocod SEGMENT ;define a segment
assume cs:hellocod, ds:hellodat, ss: hellostk
START: mov ax, hellodat ;ax <-- data segment start address
mov ds, ax ;ds <-- initialize data segment register
mov ah, dos_print ;ah <-- 9 DOS 21h string function
mov dx,OFFSET strng ;dx <-- beginning of string
int 21h ;DOS service interrupt
mov ax, 4c00h ;ax <-- 4c DOS 21h program halt function
int 21h ;DOS service interrupt
hellocod ENDS
END START

## Slide 122: Yet another way to define Segs
;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;
; Use .stack,.data,.code directives to define segment types ;
; ;
;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;
.stack 100h ; reserve 256 bytes of stack space
.data
dos_print EQU 9 ;define a constant
strng DB 'Hello World',13,10,'$' ;Define the character string
.code
START: mov ax, SEG strng ;ax <-- data segment start address
mov ds, ax ;ds <-- initialize data segment register
mov ah, dos_print ;ah <-- 9 DOS 21h string function
mov dx,OFFSET strng ;dx <-- beginning of string
int 21h ;DOS service interrupt
mov ax, 4c00h ;ax <-- 4c DOS 21h program halt function
int 21h ;DOS service interrupt
END START

## Slide 123: Program Statements
name operation operand(s) comment
Operation is a predefined or reserved word
  mnemonic - symbolic operation code
  directive - pseudo-operation code
Space or tab separates initial fields
Comments begin with semicolon
Most assemblers are not case sensitive

## Slide 124: Program Data and Storage
Pseudo-ops to define data or reserve storage
  DB - byte(s)
  DW - word(s)
  DD - doubleword(s)
  DQ - quadword(s)
  DT - tenbyte(s)
These directives require one or more operands
  define memory contents
  specify amount of storage to reserve for run-time data

## Slide 125: Defining Data
Numeric data values
  100 - decimal
  100B - binary
  100H - hexadecimal
  '100' - ASCII
  "100" - ASCII
Use the appropriate DEFINE directive (byte, word, etc.)
A list of values may be used - the following creates 4 consecutive words
  DW 40CH,10B,-13,0
A ? represents an uninitialized storage location
  DB 255,?,-128,'X'

## Slide 126: Naming Storage Locations
Names can be associated with storage locations
  ANum DB -4
  DW 17
  ONE
  UNO DW 1
  X DD ?
These names are called variables
ANum refers to a byte storage location, initialized to FCh
The next word has no associated name
ONE and UNO refer to the same word
X is an unitialized doubleword

## Slide 127: Arrays
Any consecutive storage locations of the same size can be called an array
  X DW 40CH,10B,-13,0
  Y DB 'This is an array'
  Z DD -109236, FFFFFFFFH, -1, 100B
Components of X are at X, X+2, X+4, X+8
Components of Y are at Y, Y+1, …, Y+15
Components of Z are at Z, Z+4, Z+8, Z+12

## Slide 128: DUP
Allows a sequence of storage locations to be defined or reserved
Only used as an operand of a define directive
DB 40 DUP (?)
DW 10h DUP (0)
DB 3 dup ("ABC")

## Slide 129: Word Storage
Word, doubleword, and quadword data are stored in reverse byte order (in memory)
Directive Bytes in Storage
DW 256 00 01
DD 1234567H 67 45 23 01
DQ 10 0A 00 00 00 00 00 00 00
X DW 35DAh DA 35
  Low byte of X is at X, high byte of X is at X+1

## Slide 130: Named Constants
Symbolic names associated with storage locations represent addresses
Named constants are symbols created to represent specific values determined by an expression
Named constants can be numeric or string
Some named constants can be redefined
No storage is allocated for these values

## Slide 131: Equal Sign Directive
name = expression
  expression must be numeric
  these symbols may be redefined at any time
  maxint = 7FFFh
  count = 1
  DW count
  count = count * 2
  DW count

## Slide 132: EQU Directive
name EQU expression
  expression can be string or numeric
  Use < and > to specify a string EQU
  these symbols cannot be redefined later in the program
  sample EQU 7Fh
  aString EQU <1.234>
  message EQU <This is a message>

## Slide 133: Data Transfer Instructions
MOV target, source
  reg, reg
  mem, reg
  reg, mem
  mem, immed
  reg, immed
Sizes of both operands must be the same
reg can be any non-segment register except IP cannot be the target register
MOV's between a segment register and memory or a 16-bit register are possible

## Slide 134: Sample MOV Instructions
b db 4Fh
w dw 2048
mov bl,dh
mov ax,w
mov ch,b
mov al,255
mov w,-100
mov b,0
When a variable is created with a define directive, it is assigned a default size attribute (byte, word, etc)
You can assign a size attribute using LABEL
  LoByte LABEL BYTE
  aWord DW 97F2h

## Slide 135: Addresses with Displacements
b db 4Fh, 20h, 3Ch
w dw 2048, -100, 0
mov bx, w+2
mov b+1, ah
mov ah, b+5
mov dx, w-3
Type checking is still in effect
The assembler computes an address based on the expression
NOTE: These are address computations done at assembly time MOV ax, b-1 will not subtract 1 from the value stored at b

## Slide 136: eXCHanGe
XCHG target, source
  reg, reg
  reg, mem
  mem, reg
MOV and XCHG cannot perform memory to memory moves
This provides an efficient means to swap the operands
  No temporary storage is needed
  Sorting often requires this type of operation
  This works only with the general registers

## Slide 137: Arithmetic Instructions
ADD dest, source
SUB dest, source
INC dest
DEC dest
NEG dest
Operands must be of the same size
source can be a general register, memory location, or constant
dest can be a register or memory location
  except operands cannot both be memory

## Slide 138: Program Segment Structure
Data Segments
  Storage for variables
  Variable addresses are computed as offsets from start of this segment
Code Segment
  contains executable instructions
Stack Segment
  used to set aside storage for the stack
  Stack addresses are computed as offsets into this segment
Segment directives
  .data
  .code
  .stack size

## Slide 139: Memory Models
.Model memory_model
  tiny: code+data <= 64K (.com program)
  small: code<=64K, data<=64K, one of each
  medium: data<=64K, one data segment
  compact: code<=64K, one code segment
  large: multiple code and data segments
  huge: allows individual arrays to exceed 64K
  flat: no segments, 32-bit addresses, protected mode only (80386 and higher)

## Slide 140: Program Skeleton
.model small
.stack 100H
.data
;declarations
.code
main proc
;code
main endp
;other procs
end main
Select a memory model
Define the stack size
Declare variables
Write code
  organize into procedures
Mark the end of the source file
  optionally, define the entry point